## Slide 1: Path to PED compliance of Cryo systems
04/09/2025

## Slide 2
Intro project
PED compliance Cryo Module
PED compliance Cryo System

## Slide 3
Purpose:
  ADS technology demonstrator at pre-industrial scale
  Flexible irradiation facility (Radio isotope production, reactor fuel research, …)
At SCK CEN – the Belgian nuclear research center
SUBCRITICAL REACTOR (~70MWth)
600 MeV Protons, 4mA - CW
MTBF > 250h for beam trips over 3s
3 types of SC-cavities
MYRRHA, project introduction

## Slide 4: MYRRHA, a phased approach
Phase 3 - Reactor
Phase 1 - 100 MeV
Phase 2 - 600 MeV
Phase 1 – currently being Constructed
Linear Particle Accelerator
100 MeV Protons, 4mA

## Slide 5
Building & infrastructure
RF GALLERY
Accelerator utilities
CRYO
stack
User building
Central building

## Slide 6
Injector
The Superconducting RF LINAC
QM
30 Cryomodules along the LINAC
All QM’s are identical
Low-beta LINAC
Beam direction
16.6 MeV
100 MeV
To the Application Centers
Cryomodule (QM)
→ each QM contains 2 cavities (CAV)

## Slide 7: CryoModule (QM)
Chimney (jumper connection)
Helium bath at 2 Kelvin
Beam pipe
RF Cavities
(CAV)
Tuning
System (TUN)
Magnetic Shield
(MGS)
QMST
Thermal shield
QM
RF Coupler
(CPLR)
To the Valve Box (QVB)
QM Facts
30 identical pieces
Dimensions:
Diameter - 1.3 m
Length - 2.2 m
2x supercondictive cavities (CAV) per QM operating temperature 2K
Cooling medium: Liquid He
Pressure Beam pipe: <1E-8 mbara
Pressure QMST (insulating): 1E-6 mbara
Since we have vacuum, we always use ABSOLUTE pressure in our specs/documentation

## Slide 8
QSYS – System Breakdown
QVB
QVB
QVE
QLM
QRB
WCS
WSH
WSH
WSH
QM
QM
QCELL
WPS
Cryoplant & Infrastructure
Cryo Distribution Backbone
Cryomodules QM
(30x)

## Slide 9: CryoModule (QM)

## Slide 10: CryoModule (QM)
Chimney (jumper connection)
Helium bath at 2 Kelvin
Beam pipe
RF Cavities
(CAV)
Tuning
System (TUN)
Magnetic Shield
(MGS)
QMST
Thermal shield
QM
RF Coupler
(CPLR)
To the Valve Box (QVB)

## Slide 11: QM – Volumes
Q1
P
L1
L2
M
XM
MX
Name | Volume (L) 10% error possible
Q1 | 1935
L1 | 26.5
L2 | 26.5
M | 8.4 (liquid He volume) 26.8 (vessel volume)
P | 124.2
P = BVAC volume
L, M = Helium bath volume
Q = INVAC volume, corresponds to Q1 for the QM

## Slide 12: QM – Pressures
Q1
P
L1
L2
M
XM
MX
MV1
MV2
BD561
BD560
SV590
Name | MAWP (bara)
Q1 | 1.5
L1 | 2
L2 | 2
M | 2
P | 2
P = BVAC volume
L, M = Helium bath volume
Q = INVAC volume, corresponds to Q1 for the QM
NFS scope

## Slide 13: QM – Pressures
Q1
P
L1
L2
M
XM
MX
MV1
MV2
BD561
BD560
SV590
Pressure safety device | Opening/Burst pressure (bara)
SV 590 | 1.1 – 1.5
BD 560 & 561 | 2.0
P = BVAC volume
L, M = Helium bath volume
Q = INVAC volume, corresponds to Q1 for the QM
NFS scope

## Slide 14: PID ALX/55801725
QMST tender ALX/43737760

## Slide 15: CryoModule (QM) – PED compliance
Context
The cryomodule is not supplied to SCK CEN by a single supplier
  Pressurized equipment involved:
    CAV  supplied by contractor X
    QMST  supplied by contractor Y
  - QM assembly  done by a contractor Z
Contractor contractually not required to follow PED Technically not possible to pressure test as this would deform the geometry and cause an offset in resonance frequency rendering the cavity useless
Contractor contractually required to apply PED
Contractor contractually required to apply PED

## Slide 16: CryoModule (QM) – PED compliance
What is needed to declare PED compliance (by SCK CEN) for the cryo module assembly?
PED category to be determined ?
Technical file content ?

## Slide 17
Cryogenic system – PED compliance
QVB
QVB
QVE
QLM
QRB
WCS
WSH
WSH
WSH
QM
QM
Cryo Plant
Cryo Distribution Backbone (QDB)
Cryomodules QM (30x)
Cryo Plant comes with it’s own EU declaration of conformity for PED provided by contractor
QDB comes with it’s own EU declaration of conformity for PED provided by contractor
QM comes with a EU declaration of conformity for PED self declared by SCK CEN

## Slide 18
Cryogenic system – PED compliance
QVB
QVB
QVE
QLM
QRB
WCS
WSH
WSH
WSH
QM
QM
Cryo Plant
Cryo Distribution Backbone
Cryomodules QM (30x)
What is needed to declare PED compliance (by SCK CEN) for the complete Cryo System?
What is the minimum content of the technical file?
  Is there any specific documentation that we need to receive from the contractors? Test reports, material certificates, …
  Are there any tests required on the assembled system to be carried out onsite (in Mol) ?
Cryogenic system

## Slide 19
Copyright © SCK CEN
PLEASE NOTE!
This presentation contains data, information and formats for dedicated use only and may not be communicated, copied, reproduced, distributed or cited without the explicit written permission of SCK CEN. If this explicit written permission has been obtained, please reference the author, followed by ‘by courtesy of SCK CEN’.
Any infringement to this rule is illegal and entitles to claim damages from the infringer, without prejudice to any other right in case of granting a patent or registration in the field of intellectual property.
SCK CEN
Belgian Nuclear Research Centre
Foundation of Public Utility
Registered Office: Avenue Herrmann-Debrouxlaan 40 – BE-1160 BRUSSELS
Operational Office: Boeretang 200 – BE-2400 MOL

## Slide 20
QM – Pressure differences
Q
P
L
Z
Footnote
2b, L: Capped by CV560
3a/b, L: Capped by BD560&1
3b, Q: Capped by INVACs BD
ALX/91198270

## Slide 21
Cryo-Cell (QCELL)
Cavity assy (2x)
Cavity (CAV)
Coupler (CPLR)
Cryostat (QMST)
Valve-box assy
Vacuum Vessel
Vacuum Vessel
Jumper
Vacuum Barrier
Cryomodule (QM)
Valve box (QVB)
Cold Tun. Syst. (TUN)
Cryogenic tank+pipes
Thermal Shield
Mag. Shield (MGS)
SBS Breakdown
The Cryocell (QCELL)
TUN
CPLR
CAV
MGS
QMST