## Slide 1: QSYS – ATS Database Management System
ACR Unit

## Slide 2
Background information (from other presentations)

## Slide 3
Buildings - Level 0
6
5
4
1
3
2
SCK CEN/83474410
QSYS Buildings (QB_x)
High Stakes:
Main Equipment installed on premise
Low Stakes:
Only peripherals or routing pipes
7
# | Building | QSYS top-level (*main) | QSYS Equipment
QB_1 | LTU/interior | QCELL* QDIST QINFRA | QM QVB QVE QLM WPS
QB_2 | LTU/Chicane | QDIST* QINFRA | QLM WPS
QB_3 | SAB2/RF-Gallery | QDIST* QINFRA | QLM WPS
QB_4 | SAB2/QRB Room | QPLANT QDIST QINFRA | QRB WPS QLM
QB_5 | SAB2/Other | QPLANT QINFRA? | WCS WPS?
QB_6 | SAB1/CCB | QPLANT QINFRA | WCS WSH
QB_7 | LTU/vents | QINFRA | WPS
QB_8 | SAB2/RF-Gallery | QCELL QDIST QINFRA | QC_int
QSYS is spread across SAB1, SAB2, and LTU
QSYS has high stakes when main equipment is installed, and low stakes when it is used for routing or peripherals
8

## Slide 4
QSYS Buildings
=NA.BA_CDA514-Building layout NF ACC - Plan-level 0
6
5
4
1
3
2
8
7

## Slide 5: Primary-system mnemonics (1)
Full Mnemonics of the cryomodule at this particular section/sub-section:
LB-S03:CRYO-QM-01
X – X : X – X – ##
Sub-section (i.e. S03)
Discipline (i.e. CRYO)
Device Class (i.e. QM)
Suffix (01-99)
ACC naming convention
Section (i.e. LB)
X – X
Device Class (i.e. QM)
Device Sub-class (i.e. LB)
Different types of the same device class are distinguished by their “sub-class”
All cryomodules containing “low-beta single-spoke cavities” are of class/sub-class:
QM-LB
The suffix “01” indicates that this is the 1st QM in the sub-section “LB-S03”. Sidenote: the LINAC has exactly one QM per section)
Sub-section of the low-beta LINAC (“LB-Sxx”)
Beam direction
0+24 QMs (current implementation)
LB-S30
LB-S01
0+30 QMs (Full MINERVA LINAC)
Injector
To the target facilities
QLR
Based on ACC Layout SCK/37633125 v3.0
QLM
Entrance LINAC tunnel
Cryomodule (QM)
→ each QM contains 2 cavities (CAV)
Cryo-Cell
(QCELL)
Valve box (QVB)
End-Box (NA.CP02.QVE)
Cryo-distribution line (NA.CP02.QLR+QLM)
(Only Helium is used as the cooling fluid)
Storage
(NA.CP03.xSx)
Cryoplant (NA.CP01)

## Slide 6
QSYS info for the DMS

## Slide 7: Status: 2nd ACC meeting 2025
Property Name | Data Type | Unit | Status | Value
ElementOwner | String |  |  | 
WindchillNo | String |  |  | 
InputVoltage | Float | V |  | 
InputCurrent | Float | A |  | 
EarthingTopology | String | (3)PH-N-PE |  | 
RatedElectricalInputPowerApparent | Float | VA |  | 
RatedElectricalInputPowerActive | Float | W |  | 
ActivePowerFullBeam | Float | W |  | 
CoolingWaterInletTemperatureMin | Float | degC |  | 
CoolingWaterInletTemperatureMax | Float | degC |  | 
CoolingWaterInletTemperatureFluct | Float | degC |  | 
CoolingWaterType | String |  |  | 
CoolingWaterInletPressureMin | Float | barg |  | 
CoolingWaterInletPressureMax | Float | barg |  | 
CoolingWaterPressureDropNom | Float | bar |  | 
CoolingWaterFlowNom | Float | l.min-1 |  | 
CoolingPower | Float | W |  | 
CompressedAirInletPressureMin | Float | barg |  | 
CompressedAirInletPressureMax | Float | barg |  | 
CompressedAirInletPressureNom | Float | barg |  | 
CompressedAirVolumetricFlowRateNom | Float | m3.h-1 |  | 
CompressedAirVolumetricFlowRateMax | Float | m3.h-1 |  | 
VolumetricFlowRateDurationMax | Float | s |  | 
RatedHeatDissipationToWater | Float | W |  | 
RatedHeatDissipationToAir | Float | W |  | 
OperationalTemperatureMin | Float | degC |  | 
OperationalTemperatureMax | Float | degC |  | 
OperationalHumidityMin | Float | percent |  | 
OperationalHumidityMax | Float | percent |  | 
WaterConnectionType | String |  |  | 
WaterConnectionDiameter | Float | inch |  | 
WaterConnector | String |  |  | 
Make sure all mandatory field are filled: General, Power, Cooling, Pneumatics and HVAC
   Status set to:
    ‘Y’ if value is definite
    ‘N’ if value is preliminary
    ‘NA’ if Not Applicable
If a pipe/hose connection is needed for gas(+air) and/or water, 3 additional properties can be specified, using ‘Water’ and ‘Gas’ prefix:
  ConnectionType: Flange or Twin ferrule tube fitting with NPT thread, ISO thread, BSPP thread, BSPT thread, SAE/MS straight thread, welding end
  ConnectionDiameter: inner diameter in inches
  Connector: specification in detail, so it is clear for NFS which counterpart needs to be foreseen. E.g. for cooling connections of SSA: PN40 EN 1092-1, DN 50 (Heco__FL-060-040-4)
Deadline: End of May
Still to be completed:
CRYO
Power VAC controllers
BD electronics
RFQ
CAV HVAC requirements

## Slide 8
LB-Sxx:QMST-01:CV-123
LB-Sxx = the section of the linac, from 00-30
QMST-01 = the QMST component on that section. We only have 1x QMST per section, so it is always QMST-01
CV-123 = The component in question. In this case I am imposing (for now) to match our instrumentation naming convention, so we keep the numbering as we like. For the database, there is no sub-classes (tbc)
Notes
Section LB-S01 contains also the QVE
The QLM outside of LTU (chicane and AUB) will have another section (not LB-xxx)
To be clarified
Where do we put the QLM within the LTU?
  LB-S01 or LB-TS? Up to Lennert to define

## Slide 9
LB-Sxx:CRYO-QM-01:CV123
LB-Sxx = the section of the linac, from 00-30
CRYO-QM-01 = the QMST component on that section. We only have 1x QMST per section, so it is always QMST-01
CV123 = The component in question. In this case I am imposing (for now) to match our instrumentation naming convention, so we keep the numbering as we like. For the database, there is no sub-classes (tbc)
LB-Sxx
QM-LB-25
TT123
Class/sub-class: TT-CX
Functional location shown on PID
LB-Sxx:CRYO-QM-01
Cryomodule slot
CRYO-QM-01
(instance)

## Slide 10
WPS
QLM
QRB
WSH
WCS
QVB
QMST
CAV
MGS
TUN
CPLR
QVE
CAV
MGS
TUN
CPLR
24x QCELLs
QPLANT Tender Package
RFCELL scope
tbc
tbc
Cooling
HVAC
Pneumatics
Power
Cabling

## Slide 11
Not applicable ? Then e

## Slide 12
QVB
body
Arm A
Arm B
Jumper
Patchbox 1
Patchbox 2
Chimney
QMST
QMST
INVAC
AIR

## Slide 13
QMST
QMST
4x red
CV105
CV534
CV894
CV891
2x black
1x yellow
[element]
[element]

## Slide 14
QMST
CV
  Typ1
  Typ2
  Typ3
    Set
    Read
    Air
    Power
      Conductor 1
      Conductor 2
      Conductor 3
CV-Typ2-Air-Conductor1
CV-Typ2-Set
Level 1
Level 2
Level 3
Level 4
csv file
CV-Q02 (?)
For each “occurrence”
Later change to Q01, Q02, W01 …

## Slide 15: Note on utilities
Electrical power
  Supplied by the cryo cabinet not by NFS
  The cryo cabinet does need NFS
HVAC
  Not applicable
Compressed air
  Yes, valves on QMST and QVB
Water cooling
  Not on QMST
  Only on CPLR

## Slide 16
Y, NO or NA
value

## Slide 17: Connections of the QVB

## Slide 18: To do for mid-March release (15th)
QVB and QM element level
  HVAC
  Power
  Water
  Compressed
Cable list for QM and QVB
Handling of over-instrumentation
About the cabinet

## Slide 19: Use cases
Cables
  Tag